## Slide 1
XOR, XNOR, and Binary Adders
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: XOR, XNOR & Adders
This presentation will demonstrate
The basic function of the exclusive OR (XOR) gate.
The basic function of the exclusive NOR (XNOR) gate.
How XOR and XNOR gates can be used to implement combinational logic design.
How XOR gates can be using to design half and full adders.
How full adders can be implemented with Small Scale Integration (SSI) and Medium Scale Integration (MSI) logic.
How single bit half and full adders can be cascaded to make multi-bit adders.
Notes: Introductory Slide / Overview of Presentation

## Slide 3: XOR Gate – Exclusive OR
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
X
Y
Notes: Overview of basic XOR gates: Logic Symbol, Logic Expression, and Truth Table.

## Slide 4: XNOR Gate – Exclusive NOR
X | Y | Z
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X
Y
Notes: Overview of basic XNOR gates: Logic Symbol, Logic Expression, and Truth Table.

## Slide 5: Logic Design with XOR & XNOR
Example
  Algebraically manipulate the logic expression for F1 so that XOR and XNOR gates can be used to implement the function. Other AOI gates can be used as needed.
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 6: Logic Design with XOR & XNOR
Solution
Notes: This slide includes the solution to example #1. If you print handouts, do not print this page.

## Slide 7: Binary Addition
Multiple Bit Addition:
Carry
Single Bit Addition:
Cin
Cout
A
B
Sum
Notes: This slide shows the four possible combinations of adding together two single bit binary numbers and how these single bits can be cascaded into the addition of two 4-bit binary numbers. The 4-bit is just an example; we could have used 8-bits, 12-bits, etc.

## Slide 8: Two Types of Adders
Half Adder
2 Inputs (A & B)
2 Outputs (Sum & Cout)
Used for LSB only
Full Adder
3 Inputs (A, B, Cin)
2 Outputs (Sum & Cout)
Used for all other bits
Full Adder
A
B
Cin
Sum
Cout
Half Adder
A
B
Sum
Cout
Notes: Explain the two types of adders, half adder and full adder.

## Slide 9: Half Adder – Design
A | B | Sum | Cout
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Notes: This slide includes a truth table and logic equations for a half adder. Neither K-Mapping nor Boolean algebra were required because of the simplicity of the logic.

## Slide 10: Half Adder - Circuit
Notes: Logic diagram for a half adder.

## Slide 11: Full Adder – Design of Cout
 |  | V
 | 0 | 0
 | 0 | 1
 | 1 | 1
 | 0 | 1
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: Truth table for full adder and K-Map for the Cout output of the full adder.

## Slide 12: Full Adder – Design of Sum
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
 |  | V
 | 0 | 1
 | 1 | 0
 | 0 | 1
 | 1 | 0
K-Mapping did NOT help us simplify . . . Let’s try Boolean algebra.
Notes: Truth table for full adder and K-Map for the Sum output of the full adder. Note that the K-Map did not simplify the expression.

## Slide 13: Boolean Simplification of Sum
Notes: Boolean algebra simplification for the sum output of a full adder.

## Slide 14: Full Adder - Circuit
Notes: Logic diagram for a full adder.

## Slide 15: Full Adder: AOI vs. XOR
Though XOR gates can be used for implementing any
combinational logic design, their primary application is adder
circuits. Compare the AOI implementation (above) for the
sum function to the XOR implementation (below).
Notes: This slide compares the sum output of a full adder, one implemented with AOI logic, and one implemented with XOR. This illustrates why we have XOR gates.

## Slide 16: MSI Full Adder
SSI - Full Adder
MSI - Full Adder
Notes: Introduction of the 74LS183 MSI full adder

## Slide 17: Cascading Adders – Four Bits
Example: 6 + 3 = 9
General Form
Notes: This slide provides an example and general form for cascading single bit adders into four bit adders. The 4-bit adder is simply being used as an example.

## Slide 18: Four Bit Adder with SSI Logic
Full Adder
Full Adder
Full Adder
Half Adder
Notes: 4-Bit adders built with SSI. Note that the LSB only required a half adder.

## Slide 19: Four Bit Adder with MSI Logic
Full Adder
Full Adder
Full Adder
Full Adder
Notes: 4-Bit adders built with MSI. Note that the LSB is a full adder. We must contact the Cin to a logic zero (i.e., ground).